## Slide 1: DMAS: Decentralized Multiagent Simulation – Communication Architecture Restructure
Alan Aguilar Jaramillo, Ben Gorr, Chrissi Erwin, Dr Daniel Selva Valero

## Slide 2: Current Architecture Overview
Simulation Architecture
Environment
Server accessed by agents as clients
Tracks external agent state
Simulates Earth System
Controls simulation start and end
Agents
Simulation instructions received through dedicate SUB port
“Sense” environment via server requests through dedicated environment REQ port
Inter-agent communication via reconnecting REQ/REP TCP ports
Intra-agent communication modeled as asynchronous message queues (mimics internal data bus)
Agent
Environment
Other Agents
SUB
REQ
REQ
REP
Engineering Module
Science Module
Scheduler Module
-Scenario Events
-Simulation Events
-GP access info
-GS access info
-Agent access info
-Agent state info
-Measurement observation metrics info
-Measurement Request (out)
-Information Request (out)
-Measurement Results (out)
-Planner Results (out)
Event Handler
Sim Start/End
Simulation Module
-Simulation Events
-Scenario Events
-Scheduled Measurement Measurements
-Measurement Requests (out)
-Planner Results (out)
-Measurement Requests
-Information Requests
DMAS Agent Framework

## Slide 3: Current Architecture Overview
Current Inter-Agent Communications Sequence
Current Environment Sensing Sequence
Current Environment Simulation Control Sequence
Simulation Sequences

## Slide 4: Current Architecture Overview
Ground Station Node
Satellite Node
Satellite Node
Environment Server
Env-to-agent
Sensing Data
Peer-to-peer
Data or Requests
Simulation broadcast
Sim start, end, or time
Current DMAS Simulation Framework
Limitations
Environment performs two distinct roles
Controls the simulation and propagates the state of the earth system and the agents
Centralized external agent state propagator only allows for agents with fixed trajectories
  Ground Stations/Sensors and Satellites, but no UAVs
Agents have no explicit broadcast capabilities
Agents must copy and send a message n-times as to mimic a broadcast
Increases load in the network and runtime
No real-time user monitoring capabilities during the simulation
Results and logs are only printed after the simulation finalizes
Peer-to-peer
Data or Requests

## Slide 5: New Architecture
Simulation Manager
Ground Station Node
Satellite Node
Satellite Node
Satellite Node
Environment Server
Results Logger
Env-to-agent
Sensing Data
Peer-to-peer
Data or Requests
Peer broadcast
Data or Requests
Manager broadcast
Sim start, end, or time
Node Results
Node state, actions performed, events detected/measured, etc.
Simulation Manager controls nodes
Simulation start and end times
Agent synchronization routine during initialization
Publishes network information to all nodes
Results Logger tracks agents during the simulation
Agents push their results to logger as the simulation runs
Logger tracks incoming results as they are received
Environment still modeled as a server accessed by nodes
Simulates Earth system and inter-agent connectivity
Nodes “sense” the environment by requesting simulated data

## Slide 6: New Architecture
Agent Framework Architecture
Agent Node
Environment
Other Agents
REQ
PUB
Engineering Module
Science Module
Scheduler Module
-Simulation Events
-GP access info
-GS access info
-Agent access info
-Agent state info
-Measurement observation metrics info
Agent Sim Start/End
Simulation Module
-Simulation Events
-Scheduled Measurement Measurements
-Measurement Requests (out)
-Planner Results (out)
-Measurement Requests
-Information Requests
SUB
Simulation Manager
PUSH
Results Logger
-Agent State
-Planner Results (in)
-Measurement Requests (in)
-Measurement Data (out)
-Measurement Results (from self or other agents)
-Information Request
-Agent State
-Actions performed
-Events detected/measured
-Measurement Requests
-Information Requests
-Measurement Results
-Planner Results
Agent
Environment
Other Agents
SUB
REQ
REQ
REP
Engineering Module
Science Module
Scheduler Module
-Scenario Events
-Simulation Events
-GP access info
-GS access info
-Agent access info
-Agent state info
-Measurement observation metrics info
-Measurement Request (out)
-Information Request (out)
-Measurement Results (out)
-Planner Results (out)
Event Handler
Sim Start/End
Simulation Module
-Simulation Events
-Scenario Events
Current DMAS Agent Framework
Redeveloped DMAS Agent Framework

## Slide 7: New Architecture
Agent Framework Architecture
New broadcast capabilities
Inter-Agent communication handled via PUB/SUB port
Agents subscribe to messages addressed directly to them or to ‘ALL’
Connection to other agent’s PUB ports dynamically controlled by the Environment
Agent Node
Environment
Other Agents
REQ
PUB
Engineering Module
Science Module
Scheduler Module
-Simulation Events
-GP access info
-GS access info
-Agent access info
-Agent state info
-Measurement observation metrics info
Agent Sim Start/End
Simulation Module
-Simulation Events
-Scheduled Measurement Measurements
-Measurement Requests (out)
-Planner Results (out)
-Measurement Requests
-Information Requests
SUB
Simulation Manager
PUSH
Results Logger
-Agent State
-Planner Results (in)
-Measurement Requests (in)
-Measurement Data (out)
-Measurement Results (from self or other agents)
-Information Request
-Agent State
-Actions performed
-Events detected/measured
-Measurement Requests
-Information Requests
-Measurement Results
-Planner Results
Redeveloped DMAS Agent Framework

## Slide 8: New Architecture
Redeveloped Inter-Agent Communications Sequence
Redeveloped Environment Sensing Sequence
Redeveloped Simulation Manager Control Sequence
Simulation Sequences

## Slide 9: Discussion
Add external state propagating capabilities to agents?
Agents’ engineering module would be in charge of propagating external state
  Position, velocity, ground coverage, etc.
Would allows for on-line position propagation
  Useful for UAV path propagation and orbital maneuvers
Creates issues for the environment to track ground coverage and inter-agent access times
  All satellites should inform the environment of their orbital parameters at the beginning of the simulation/whenever a maneuver is performed?
  What about for coverage and access from satellites to UAVs?

## Slide 10: Questions?