## Slide 1: DMAS Decentralized Multi-Agent Satellite System Simulation
Alan Aguilar Jaramillo

## Slide 2: Overview
Motivation
Program Iterations
Agent Representation
Program Architecture
  SimPy as a Multi-Agent Simulator
  Program workflow
  Program structure
Development Status
Future Work

## Slide 3: Motivation
Previous Work on Planners
Market-based planner for distributed systems (MCCBBA)
Allowed for collaboration and partial task completion between agents
Assumed 2D world with constant communications
No astrodynamics considered
Astrodynamics-related Constraints
Orbit-dependent limits on access times to measurements
Earth’s dynamic environment can create areas of interest for measurements
Constant communication between satellites and ground stations is not guaranteed
Onboard computational power in satellites is limited
Goals: create a tool to simulate distributed satellite systems and test various planning algorithms
Planning: What satellite does what and when?
1
2
3
4
2
1
3
4
4
2
2

## Slide 4: Program Iterations
Old - Java
Used lab’s orekit toolbox for astrodynamics
Fixed time-step approach
Computationally and memory expensive
Long events consisted of multiple single-time-step events
Hard to capture transience happening between steps
New - Python
Improve collaboration with external people
Based on SimPy
Uses discreet event structure
Allows for event-driven agents

## Slide 5: Agent Representation
Agent
Environment / Other Agents
Sense
Think
Do
Planner
Knowledge Base
Intelligent Agents
Can perceive their environment
Can make decisions on what actions to perform
Actions affect the environment, other agents, or the agent itself
Satellites, Ground Stations, and Aircraft all treated as intelligent agents

## Slide 6: Agent Representation
Agent
Environment / Other Agents
Sense
Think
Do
Planner
Knowledge Base
Agents
In charge of perceiving information from its environment or receiving information from other agents
Thinking Phase asks planner what to do
Performs actions given by the planner
Tracks current state and execution of tasks
Planner
Processes information from agent
Maintains an internal knowledge base
Determine the next set of actions to be performed by the agent
Interacts with the agent via actions given
Satellites, Ground Stations, and Aircraft all treated as intelligent agents
Actor
Planning

## Slide 7: Program Architecture
SimPy as a Multi-Agent Simulator
Designed for scheduling concurrent processes
  Processes are actions that can take a non-zero amount of time to perform
  Processes can sometimes have dependencies on each other
    i.e. “Process A cannot start until processes B and C are both done”
  Wait-timers with delayed execution
Allows for shared resources between processes
  Containers and Stores
    Containers – hold/track a non-zero quantity (integer or real number)
    Stores – hold/track non-integer objects
  Resources can be requested and can wait until the desired amount or type of resources are available
Process A
Process B
Process C
Example of delayed execution with dependencies

## Slide 8: Program Architecture
SimPy as a Multi-Agent Simulator
Internal Resources
Internal Memory (Container)
Battery Charge (Container)
Message Inbox (Store)
Actions represented as internal processes
Background tasks
  Listen – lookout for incoming transmissions
  System Check – check agent’s health
  Wait for planner – wait for instructions from planner
Maintenance tasks
  Actuate components on and off
  Place agent in safe-mode
Action tasks
  Perform measurements
  Charge Batteries
  Send Message to another agent
Agents are represented as concurrent processes interacting with their environment represented as shared resources
measurement()
listen()
system_check()
listen()
planner_wait()
system_check()
Example of an Agent’s internal processes

## Slide 9: Program Architecture
Agent
Environment / Other Agents
Sense
Think
Do
Planner
Knowledge Base
Description
Performs simultaneous actions until one of them is terminated. It then informs the planner and moves on to the doing phase
Simultaneous Actions
Wait for planner instructions
Listen for incoming messages
Perform Systems-Check
Planner Wait
Listen
Systems Check
  Program Workflow
Future state model

## Slide 10: Program Architecture
Agent
Environment / Other Agents
Sense
Think
Do
Planner
Knowledge Base
Description
Performs all actions instructed by the planner while also performing background tasks in the background.
Once it is done, it informs the planner and returns to the sense/think phase.
Simultaneous Actions
Perform planner actions
Listen for incoming messages
Perform Systems-Check
Perform Actions
Listen
Systems Check
  Program Workflow

## Slide 11: Program Architecture
Program Structure
Agent
List<Component> component_list
State state
Environment env
int unique_id
Planner planner
Store<Action> plan_inbox
List<Action> actions
Logger logger
live()
perform_maintenance_actions()
actuate_agent(action)
actuate_component(action)
delete_mst(msg)
measure(action)
transmit(action)
charge(action)
wait_for_plan()
listening()
system_check()
update_components()
is_in_critical_state()
Component
string name
bool status
bool health
double power
container energy_stored
double energy_capacity
double data_rate
container data_stored
double data_capacity
is_on()
turn_on()
turn_off()
Transmitter
double max_data_rate
int num_channels
resource channels
send_message(env, msg)
Receiver
double max_data_rate
int num_channels
resource channels
Store inbox
receive(env, msg)
Power Generator
double max_power_generation
turn_on_generator(power_out)
turn_off_generator()
On Board Computer
Battery
double max_power_generation
double dod
bool charging
turn_on_generator(power_out)
turn_off_generator()
Instrument

## Slide 12: Program Architecture
Program Structure
Agent
List<Component> component_list
State state
Environment env
int unique_id
Planner planner
Store<Action> plan_inbox
List<Action> actions
Logger logger
live()
perform_maintenance_actions()
actuate_agent(action)
actuate_component(action)
delete_mst(msg)
measure(action)
transmit(action)
charge(action)
wait_for_plan()
listening()
system_check()
update_components()
is_in_critical_state()
State
Agent parent_agent
List<double> data_rate_in
List<double> data_memory
List<double> data_rate_out
double data_capacity
List<double> power_in
List<double> power_out
List<double> power_tot
List<double> energy_stored
double energy_capacity
List<double> t
Map<Component,List<bool>> isOn
bool critical
update(t)
Is_critical()
get_last_update_time()
get_state_by_intex()
get_latest_state()
Note: state gets updated at the beginning and the end of each process

## Slide 13: Program Architecture
Program Structure
Agent
List<Component> component_list
State state
Environment env
int unique_id
Planner planner
Store<Action> plan_inbox
List<Action> actions
Logger logger
live()
perform_maintenance_actions()
actuate_agent(action)
actuate_component(action)
delete_mst(msg)
measure(action)
transmit(action)
charge(action)
wait_for_plan()
listening()
system_check()
update_components()
is_in_critical_state()
Planner
Environment env
List<Process> plan
List<Process> active_plan
List<Process> completed_plan
List<Process> interrupted_plan
KnowledgeBase kb
update(state, t)
schedule_action(action, state, t)
completed_action(action, state, t)
interrupted_action(action, state, t)
interrupted_message(msg, t)
timed_out_message(msg, t)
received_message(msg, t)
deleted_message(msg, t)
update_knowledge_base(result)

## Slide 14: Program Architecture
Program Structure
Agent
List<Component> component_list
State state
Environment env
int unique_id
Planner planner
Store<Action> plan_inbox
List<Action> actions
Logger logger
live()
perform_maintenance_actions()
actuate_agent(action)
actuate_component(action)
delete_mst(msg)
measure(action)
transmit(action)
charge(action)
wait_for_plan()
listening()
system_check()
update_components()
is_in_critical_state()
Action
string type
double start
double end
is_active()
is_done()
ActuateAgentAction
bool status
ActuateComponentAction
bool status
Component component
ActuatePowerCompAction
double power
DeleteMessageAction
Message msg
MeasurementAction
List<Component> instrument_list
Target target
TransmitAction
Agent src
Agent dst
String message_id
Message msg
ChargeAction

## Slide 15: Development Status
Feature | Status | Notes
Agent Live | Undergoing testing | -
Agent State Tracking | Power-tracking implemented and tested. Data-tracking implemented but pending tests | Does not yet track satellite position, velocity or attitude
Message Transmission | Pending testing | -
Planner | Abstract object implemented | Only unit-test planners exist so far. No measurement planning nor knowledge-base yet. Rescheduling capabilities missing.
Astrodynamics | Implemented for comms. Pending testing | Only used to determine how long an agent must wait until the next access with its target. Position, velocity, and eclipse information not yet implemented.
Outputs | Implemented and Tested | Outputs state history as a csv and each agent’s action log as separate files. Satellite position and velocity not yet outputted.
Visualizer | Implemented | Basic plotter for power and data-rate tracking

## Slide 16: Future Work
Finish Simulation Framework
  Communications unit-test
  Track and output communications delays
  Fix simultaneous process timing bugs
  Implement and test 3D-CHESS scenario onto DMAS
  Data, position, velocity, attitude, and eclipse tracking
  Output orbital position and velocity for satellite agents
  Create formal SatelliteAgent and GroundStationAgent classes from Agent class
    Agents keep track of orbital parameters and may have battery power restrictions. Measurements limited by orbit and instruments
    Ground station agents have no power restrictions. Measurements limited by ground location and instruments
  Test with 3D-CHESS scenario onto DMAS
Implement Planners
  MDP
  Centralized Planner (Rich or MILP?)
  CCBBA
Implement Knowledge Base
  Develop or Implement
  Unit-test
Implement Measurement Performance Simulation
  Quantify predicted utility of a measurement
  Simulate measurement performance (InstruPy)
Perform Tests
  Use centralized planner to unit-test framework
  Compare planner performance
Increase Satellite capability
  Attitude and orbit changes

## Slide 17: Questions?